| Part 43 MAINTENANCE, PREVENTIVE MAINTENANCE, REBUILDING, AND ALTERATION |
| --- |
| Appendix A--Major Alterations, Major Repairs, and Preventive Maintenance |  |

Appendix A

Sec. A43.1

(c) Preventive maintenance. Preventive maintenance is limited to the following work, provided it does not involve complex assembly operations:

(5) Replacing defective safety wiring or cotter keys.
(6) Lubrication not requiring disassembly other than removal of nonstructural items such as cover plates, cowlings, and fairings.
(7) Making simple fabric patches not requiring rib stitching or the removal of structural parts or control surfaces. In the case of balloons, the making of small fabric repairs to envelopes (as defined in, and in accordance with, the balloon manufacturers' instructions) not requiring load tape repair or replacement.
(9) Refinishing decorative coating of fuselage, balloon baskets, wings tail group surfaces (excluding balanced control surfaces), fairings, cowlings, landing gear, cabin, or cockpit interior when removal or disassembly of any primary structure or operating system is not required.
(10) Applying preservative or protective material to components where no disassembly of any primary structure or operating system is involved and where such coating is not prohibited or is not contrary to good practices.
(11) Repairing upholstery and decorative furnishings of the cabin, cockpit, or balloon basket interior when the repairing does not require disassembly of any primary structure or operating system or interfere with an operating system or affect the primary structure of the aircraft.
(15) Replacing seats or seat parts with replacement parts approved for the aircraft, not involving disassembly of any primary structure or operating system.
(16) Trouble shooting and repairing broken circuits in landing light wiring circuits.
(17) Replacing bulbs, reflectors, and lenses of position and landing lights.
(21) Replacing any hose connection except hydraulic connections.
(22) Replacing prefabricated fuel lines.
(24) Replacing and servicing batteries.
(25) Cleaning of balloon burner pilot and main nozzles in accordance with the balloon manufacturer's instructions.
(26) Replacement or adjustment of nonstructural standard fasteners incidental to operations.
(27) The interchange of balloon baskets and burners on envelopes when the basket or burner is designated as interchangeable in the balloon type certificate data and the baskets and burners are specifically designed for quick removal and installation.